## Slide 1
RMTC Lab Research Evaluation
Hierarchical Federated Learning for Privacy-Aware, Low-Latency Multimodal IoT Systems
Student:
Samartha H V | Regd. 251580130019
Programme:
M.Tech CSE — MIT Bengaluru
Guide:
Dr. Shreyas J
Industry:
Mr. Tejas J (Capgemini)
Date:
April 24, 2026
MIT Bengaluru | Department of Computer Science & Engineering

## Slide 2
Introduction
Problem Statement & Motivation
The Problem
▸ 2.5 Billion healthcare IoT devices by 2027
▸ Raw patient data (ECG, X-ray) cannot leave hospital
▸ Centralised ML violates patient privacy (HIPAA/GDPR)
▸ High communication cost sending data to cloud
▸ Latency unacceptable for real-time clinical decisions
The Solution — Hierarchical FL
▸ Devices train locally — raw data never shared
▸ Only model updates (gradients) are transmitted
▸ Two-tier hierarchy: Device → Edge → Cloud
▸ Differential Privacy (DP-SGD) guarantees privacy
▸ Top-k sparsification reduces communication by 76%
Research Scope — Healthcare Domain
Modality A
PTB-XL ECG (12-lead Signal)
Modality B
Kermany Chest X-Ray (RGB Image)
Modality C
PTB-XL Metadata (Tabular)
Devices
6 IoT Devices 2 Edge Servers
Samartha H V | MIT Bengaluru | M.Tech CSE | 2026

## Slide 3
Literature Survey & Research Gaps
What exists and what is missing
Reference
Method
Limitation
McMahan et al. 2017 (FedAvg, AISTATS)
Single-tier federated averaging
No hierarchy, no DP, single modality
Li et al. 2020 (FedProx, MLSys)
Proximal term for non-IID data
No multimodal support, no privacy
Abadi et al. 2016 (DP-SGD, CCS)
Differential privacy for deep learning
Not applied in federated multimodal setting
Qayyum et al. 2022 (Healthcare FL survey)
FL survey for medical imaging
Single modality, no ECG+X-ray fusion
MOON (Li et al. 2021)
Contrastive FL for non-IID
No DP guarantee, no hierarchy
Research Gaps Identified
▸ No FL system fuses ECG + X-ray under federated constraints
▸ DP-SGD + Top-k compression not combined in hierarchical FL
▸ Non-IID multimodal healthcare data partitioning not studied
Research Objectives
▸ Design two-tier HFL for multimodal healthcare IoT
▸ Integrate DP-SGD + Top-k for privacy + efficiency
▸ Validate on real clinical datasets (PTB-XL + CXR)
Samartha H V | MIT Bengaluru | M.Tech CSE | 2026

## Slide 4
System Architecture — HFL Framework
Two-Tier Hierarchical Federated Learning for Healthcare IoT
TIER 1 — IoT Devices
▸ 6 wearable / bedside sensors
▸ Local training with DP-SGD
▸ Top-k gradient sparsification
▸ ECG + X-ray data stays on device
TIER 2 — Edge Servers (Ward Gateway)
▸ 2 ward-level edge servers
▸ Weighted FedAvg aggregation
▸ Conformal calibration (FedConform-HC)
▸ Low-latency local aggregation
TIER 3 — Cloud Server
▸ Global model aggregation
▸ Privacy budget tracking (ε, δ)
▸ Model distribution back to edges
▸ Final evaluation & checkpointing
→
→
Model 1 — HFL-MM-HC
▸ ECG Encoder : 1D-CNN + Bidirectional GRU
▸ Image Encoder: MobileNetV3-Small (pretrained ImageNet)
▸ Fusion : Late fusion FC head with GroupNorm
▸ Privacy : DP-SGD (ε=8.0, δ=1e-5)
▸ Compression : Top-k sparsification (80%) + 8-bit quant
▸ Parameters : 2.15M total | 2.0M trainable
Model 2 — PHANTOM-FL (5 Innovations)
▸ CMGA : Cross-Modal Gated Attention (ECG ↔ X-ray)
▸ SADP : Self-Adaptive Differential Privacy
▸ ASWA : Adaptive Server-side Weight Aggregation
▸ FedKD-E : Federated Knowledge Distillation (Edge)
▸ pFAL : Personalised Federated Adapter Learning
▸ IP Claims: IP-1 through IP-10 filed
Samartha H V | MIT Bengaluru | M.Tech CSE | 2026

## Slide 5
Datasets Used
Real Clinical Datasets — Peer-Reviewed & Citable
Modality A — PTB-XL ECG (Signal)
Source
PhysioNet / Nature Scientific Data 2020
Full size
21,799 ECG records — 12 leads, 100 Hz
Subset used
5,000 records — stratified 1,000 per class
Classes
NORM · MI · STTC · CD · HYP (5 classes)
Format
WFDB (.dat + .hea) — 10 sec per record
Tensor shape
[5000, 12, 1000] float32
Tabular
Age, sex, height, weight, strat_fold (5 features)
Modality B — Kermany Chest X-Ray (Image)
Source
Cell 2018 — Kermany et al. (top-tier citation)
Full size
5,856 JPEG images
Subset used
3,000 images — balanced 1,500 per class
Classes
NORMAL (0) · PNEUMONIA (1) — binary
Format
JPEG → RGB → [3, 224, 224] float32
Tensor shape
[3000, 3, 224, 224] float32
Normalisation
ImageNet mean/std — MobileNetV3 compatible
FL Data Partitioning — Non-IID Dirichlet (α = 0.5) | 6 Devices | 2 Edge Servers | TVD = 0.4556
Device
Edge
Train
Val
Test
Device 00-02 → Edge 0 | Device 03-05 → Edge 1
Samartha H V | MIT Bengaluru | M.Tech CSE | 2026

## Slide 6
Methodology & Algorithm
Two-Tier FedAvg + DP-SGD + Gradient Compression
Algorithm: HFL-MM-HC Training (20 Global Rounds)
1
Initialise
Cloud broadcasts global model to 2 edge servers
2
Distribute
Each edge server sends model to its 3 IoT devices
3
Local Train
Each device runs DP-SGD (ε=8.0) — adds calibrated Gaussian noise to gradients
4
Compress
Top-k sparsification (80% sparse) + 8-bit quantisation before upload
5
Edge Agg
Edge server runs weighted FedAvg on received compressed gradients
6
Conform
FedConform-HC calibrates prediction sets for uncertainty quantification
7
Cloud Agg
Cloud aggregates 2 edge models → new global model (weighted by data size)
8
Evaluate
Global model evaluated on val set → log AUC, Accuracy, ε spent
9
Repeat
Steps 2–8 repeated for 5 edge rounds per global round → 20 global rounds
DP-SGD Privacy Parameters
Privacy budget ε
8.0
Privacy delta δ
1 × 10⁻⁵
Noise multiplier σ
0.5655 (auto)
Gradient clip C
1.0
Guarantee
Mathematical — not heuristic
Gradient Compression
▸ Top-k sparsification → 80% sparse
▸ 8-bit quantisation → 4× size reduction
▸ Error feedback buffer → no accuracy loss
▸ Combined saving → 76.4% comm. reduction
Samartha H V | MIT Bengaluru | M.Tech CSE | 2026

## Slide 7
Results & Expected Outcomes
Simulation Confirmed + Model Training In Progress
Simulation Results are CONFIRMED via NS-3 v3.46.1 + CloudSim Plus v8.5.6 | Model training results are EXPECTED (pipeline complete, training in progress)
Simulation Results — CONFIRMED
Metric
Achieved
Target
Status
Communication Reduction
76.4%
> 70%
Exceeded
Energy Saving
74.9%
> 70%
Exceeded
Network Reliability
99.05%
> 99%
Exceeded
Round-trip Latency
< 120ms
< 150ms
Exceeded
Expected Model Results
Metric
Expected Value
ECG Classification Acc.
82–88%
Macro AUC (5-class)
0.90–0.94
F1-Score (weighted)
0.83–0.89
Convergence
~15 rounds
Privacy (ε final)
≤ 8.0
Expected values are grounded in: Wagner et al. 2020 (PTB-XL), Nguyen et al. 2022 (Healthcare FL), McMahan et al. 2017 (FedAvg baseline)
Implementation Status
HFL Architecture
Complete
Dataset Pipeline
Complete
Model Code (GPU)
Complete
NS-3 Simulation
Complete
CloudSim Simulation
Complete
Model Training
In Progress
Final Paper
Drafting
Samartha H V | MIT Bengaluru | M.Tech CSE | 2026

## Slide 8
Novelty & Intellectual Property
10 IP Claims + 7 Novelty Contributions
IP
Name
Contribution
IP-1
FedMamba-HC
State-space model for federated ECG encoding
IP-2
FedMedLoRA
Low-rank adaptation for medical FL fine-tuning
IP-3
ClinicalCMGA
Cross-modal gated attention for ECG+X-ray fusion
IP-4
SADP
Self-adaptive differential privacy noise scheduler
IP-5
ASWA
Adaptive server-side weight aggregation
IP-6
FedKD-E
Edge-level federated knowledge distillation
IP-7
pFAL
Personalised federated adapter learning
IP-8
HFL-MM
Multimodal hierarchical FL baseline framework
IP-9
FedConform-HC
Federated conformal prediction for healthcare
IP-10
PHANTOM-FL
Full 5-innovation privacy-aware multimodal FL
Samartha H V | MIT Bengaluru | M.Tech CSE | 2026

## Slide 9
Abstract, Conclusion & References
Abstract
This research proposes a Hierarchical Federated Learning (HFL) framework for privacy-aware multimodal IoT systems in healthcare. The framework integrates a 12-lead ECG encoder (1D-CNN+GRU) with a chest X-ray encoder (MobileNetV3-Small) under a two-tier federated architecture across 6 IoT devices and 2 edge servers. Differential Privacy (DP-SGD, ε=8.0) provides mathematical privacy guarantees, while Top-k sparsification achieves 76.4% communication reduction. Simulation results confirm 74.9% energy saving and 99.05% network reliability — all exceeding design targets. Ten IP claims and seven novelty contributions are documented, targeting IEEE Transactions on NNLS (Q1).
Conclusion
▸ Complete HFL framework designed for healthcare IoT
▸ Multimodal fusion: ECG + X-ray under FL constraints
▸ Mathematical privacy guarantee via DP-SGD
▸ 76.4% comm. reduction — exceeds all targets
▸ 10 IPs filed, paper targeting Q1 IEEE journal
Future Work
▸ Complete model training & collect AUC/F1 results
▸ Implement PHANTOM-FL full 5-innovation pipeline
▸ Extend to 3rd modality (clinical notes / tabular)
▸ Deploy on Raspberry Pi edge hardware prototype
▸ Submit to IEEE Trans. NNLS / TPDS
Key References
[1] McMahan et al. — Communication-Efficient Learning of Deep Networks. AISTATS 2017.
[2] Abadi et al. — Deep Learning with Differential Privacy. CCS 2016.
[3] Wagner et al. — PTB-XL: A Large Publicly Available ECG Dataset. Sci. Data 2020.
[4] Kermany et al.— Identifying Medical Diagnoses using Deep Learning. Cell 2018.
Samartha H V | MIT Bengaluru | M.Tech CSE | 2026